Marquee Software DPB D4.80  Release Notes

Compatibility

This software is suitable only for a Deflection Processor Board (DPB) installed as part of the Control Module (CLM), part number 02-2x0306-07P (Main PCB Number 50-2006-02P).  This CLM was used in the production of Marquee 8000 and 9000 series projectors.

This software is compatible with all versions of Marquee main 68k (U35) software and with all versions of IOP (U16) software.

D4.xx or higher software versions are only compatible with DPB PCB #50-2106-05P.

About the DPB processor

The Control Module (CLM) of the Marquee series projectors is a complex electronic system. Its correct operation is critical to the performance of a Marquee.

The CLM has a smaller circuit board attached to it known as the Deflection Processor Board (DPB).  U7 on the DPB is a single chip 68HC711E9 micro-controller. The programming for U7 on the DPB is identified by its version number in the form DX.XX, for example D4.80. The intent of the “D” in the version number is to indicate that it is for the DPB.

About the changes from D4.70 to D4.80

The following change has been made for version D4.80  U7.

It now works with the Contrast Modulation Module (CMM).

If you would like to obtain the U7 D4.80 software, contact an Electrohome Service Depot. Order part number 03-00D480-01P for U7.