Re: Modifications for Using ACON With Older Marquee Projectors

The earliest Marquee projectors came equipped with Control Modules that require modifications to work correctly with Marquee ACON. There were only about 50 of these Control Modules ever sold and they can be identified by the printed circuit board number 50-2006-01P that is shown between the two card edge connectors. These older projectors were manufactured before June 1993.

Marquee projectors manufactured after June 1993 or those that contain Control Modules with the printed circuit board number 50-2006-02P (or higher) do not require any special modifications to work with ACON.

If the ACON circuit board is installed in a projector with a 50-2006-01P labeled Control Module, the projector may not power up correctly.

Qualified service personnel are welcome to perform the following modifications  that enable Marquee Control Modules labeled 50-2006-01P to function correctly with Marquee ACON.

1. Lift pin 3 of U1 (and leave it disconnected).

2. Solder a flywire from pin 5 of U2 to PC1-18. Do not lift pin 5 of U2 when doing this. PC1-18 is the 18th pin in the C row of the card edge connector nearest to C43.

In addition, to be future compatible with any digital cards in the spare slot, 50-2006-01P labeled Control Modules should be further modified as follows:

3. Move the flywire connection from pin 8 of U33 to pin 10 of U33. Do not lift pin 10 or pin 8 of U33 when doing this.

These modifications require delicate soldering work on surface mount electronic components. Please use proper Electrostatic Discharge (ESD) procedures. If you are uncomfortable with performing these modifications they can be done for you at an authorized Electrohome service depot, or simply use a newer Control Module (one that does not require modifications as described above).